## Slide 1
UCSD CSE 30
Cao Session. Slides Credit Keith Muller
Numbers Data and Memory
Computer Organization and Systems Programming
Version 2.00
Cray XMP-1982

## Slide 2: Positive Number (unsigned) in 4 bits
Real hardware has a fixed number of bits to store numbers (pi-cluster is 32 bits)
There are only distinct values in n bits
This limits the range of positive number to be 0 (unsigned min) to - 1 (unsigned max)
Hex digit | 0x0 | 0x1 | 0x2 | 0x3 | 0x4 | 0x5 | 0x6 | 0x7
Decimal value | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Binary value | 0b0000 | 0b0001 | 0b0010 | 0b0011 | 0b0100 | 0b0101 | 0b0110 | 0b0111
Hex digit | 0x8 | 0x9 | 0xa | 0xb | 0xc | 0xd | 0xe | 0xf
Decimal value | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Binary value | 0b1000 | 0b1001 | 0b1010 | 0b1011 | 0b1100 | 0b1101 | 0b1110 | 0b1111
x
umin
umax

## Slide 3: Unsigned Integers (positive numbers) with Fixed # of Bits
4 bits is = ONLY 16 distinct values
Modular (C operator: %) or clock math
  Numbers start at 0 and “wrap around” after 15 and go back to 0
Keep adding 1
wraps (clockwise)
  0000 -> 0001 … -> 1111 -> 0000
Keep subtracting 1
wraps (counter-clockwise)
  1111 -> 1110 … -> 0000 -> 1111
Addition and subtraction use normal "carry" and "borrow" rules, just operate in binary
x

## Slide 4: Unsigned Binary Number: Addition in 4 bits
0 0 0 1
0 1 1 1
0
0
1
1
1
1
1
0
+
carries
sum
Carry Bit
x
0
7
8
Be Aware in Binary
1 + 1 = 10 base 10: (1 + 1 = 2)
1 + 1 + 1 = 11 base10: (1 + 1 + 1 = 3)
=

## Slide 5: Unsigned Binary Number: Subtraction in 4 bits
0 1 0 1
0 0 1 1
1
0
5
0
1
-
Borrows
sum
x
0
3
2
Be Aware in Binary
1 - 1 = 0 base 10: (1 - 1 = 0)
10 - 1 = 1 base10: (2 – 1 = 1)
-
=

## Slide 6: Unsigned Binary Number: Addition in 4 bits – Overflow!
1 0 1 0
0 1 1 1
0
1
10
0
1
1
1
+
carries
sum
Carry Bit
x
Be Aware in Binary
1 + 1 = 10 base 10: (1 + 1 = 2)
1 + 1 + 1 = 11 base10: (1 + 1 + 1 = 3)
0
7
17
=

## Slide 7: Unsigned Binary Number: Subtraction in 4 bits – Overflow!
0 1 0 1
0 1 1 1
1
0
5
1
1
-
Borrows
sum
x
1
7
2
Be Aware in Binary
1 - 1 = 0 base 10: (1 - 1 = 0)
10 - 1 = 1 base10: (2 – 1 = 1)
=
-
1
0
1
1

## Slide 8: Overflow: Going Past the Boundary Between umax and umin
umin
umax
Overflow with unsigned numbers: Occurs when an arithmetic result (from addition or subtraction for example) is is more than min or max limits
Example shown is for a 4-bit number
x
C (and Java) ignore overflow exceptions
You end up with a bad value in your program and absolutely no warning or indication… happy debugging!….

## Slide 9: Problem: How to Encode Both Positive and Negative Integers
How do we represent the negative numbers within a fixed number of bits?
  Allocate some bit patterns to negative and others to positive numbers (and zero)
distinct bit patterns to encode positive and negative values
Unsigned values: 0 ... –1
Signed values: … –1 (dividing the range in ~ half including 0)
On a number line (below): 8-bit integers – signed and unsigned (e.g., char in C)
-
+
-1
Same “width” (same number of encodings), just shifted in value
-1
Unsigned
Signed
x
-1 comes from counting 0 as a "positive" number

## Slide 10: Negative Integer Numbers: Sign + Magnitude Method
Use the Most Significant Bit as a sign bit
  0 as the MSB represents positive numbers
  1 as the MSB represents negative numbers
Two (oops) representations for zero: 0000, 1000
Tricky Math (must handle sign bit independently)
  Positive and Negatives “increment” (+1) in the opposite directions!
Sign bit
Remaining bits
31
30
0
MSB
these numbers show bit position boundaries
LSB
x

## Slide 11: Signed Magnitude Examples (Sign bit is always MSB)
0 110
positive
6
1 011
negative
3
0 0000000
positive
0
1 0001100
negative
12
1 000 = -0
1 001 = -1
1 010 = -2
1 011 = -3
1 100 = -4
1 101 = -5
1 110 = -6
1 111 = -7
0 000 = 0
0 001 = 1
0 010 = 2
0 011 = 3
0 100 = 4
0 101 = 5
0 110 = 6
0 111 = 7
Examples (4 bits):
x

## Slide 12: Two’s Complement: The MSB Has a Negative Weight
4-bit (w = 4) weight = = -23 = -8
  10102 unsigned: 1x23 + 0x22 + 1x21 + 0x20 = 10
  10102 two’s complement: -1x23 + 0x22 + 1x21 + 0x20 = -8 + 2 = –6
  -8 in two’s complement: 10002 = -23 + 0 = -8
  -1 in two’s complement: 11112 = -23 + (23 – 1) = -8 + 7 = -1
weight is ), all other bits: have positive weights )
. . .
b0
bn-1
bn-2
x

## Slide 13: 2's Complement Signed Integer Method
Positive numbers encoded same as unsigned numbers
All negative values have a one in the leftmost bit
All positive values have a zero in the leftmost bit
  This implies that 0 is a positive value
Only one zero
For n bits, Number range is) to - 1)
  Negative values “go 1 further” than the positive values
Example: the range for 8 bits: -128, -127, .. 0, .. 126, +127
Example the range for 32 bits: -2147483648 .. 0, .. +2147483647
Arithmetic is the same as with unsigned binary!
x

## Slide 14: Summary: Min, Max Values: Unsigned and Two’s Complement
Two’s Complement Unsigned for n bits
Unsigned Value Range
  UMin = 0b00…00 =
  UMax = 0b11…11 =
Two’s Complement Range
  SMin = 0b10…00 =
  SMax = 0b01…11 =
For n=4
x

## Slide 15: Negation Of a Two’s Complement Number (Method 1)
7 = 0111
invert = 1000
add 1 + 1
-7 1001
7 = 0111
-7 = + 1001
(discard carry) 0000
-7 = 1001
invert = 0110
add 1 + 1
7 0111
1 = 0001
invert = 1110
add 1 + 1
-1 1111
-1 = 1111
invert = 0000
add 1 + 1
1 0001
-x == ~x + 1;
-8 = 1000
invert = 0111
add 1 + 1
-8 1000 oops!
x

## Slide 16: Negation of a Two’s Complement Number (Method 2)
copy unchanged right most bit containing a 1 and all the 0's to its right
Invert all the bits to the left of the right-most 1
0 1 1
1
7 =
-7 =
1 0 0
1
invert
Copy
0
1 0 0
4 =
-4 =
1
1 0 0
invert
Copy
0 0 1 1
1 0 0 0
56 =
-56 =
1 1 0 0
1 0 0 0
invert
Copy
0 0 0 0
0 =
0 =
0 0 0 0
Copy
1 0 0 0
-8 =
-8 =
1 0 0 0
Copy
OOPS!
x

## Slide 17: Signed Decimal to Two's Complement Conversion
x
dividend -102 | Quotient | Remainder | Bit Position
102/2 | 51 | 0 | b0
51/2 | 25 | 1 | b1
25/2 | 12 | 1 | b2
12/2 | 6 | 0 | b3
6/2 | 3 | 0 | b4
3/2 | 1 | 1 | b5
1/2 | 0 | 1 | b6
0/2 | 0 | 0 | b7
102(base 10) =
Get the two complement of 01100110 is 10011010

## Slide 18: Two's Complement to Signed Decimal Conversion - Positive
What is 0 1 1 0 0 1 0 1(base 2) in decimal (N)?
Signed Bit Bias | Bit | Bit Position | Bias
-2W-1 = -28-1 = -128 | x 0 | b7 | 0
Product Shift Left | Addend | Bit Position | Product
0 | + 1 | b6 | 1
2 x 1 = 2 | + 1 | b5 | 3
2 x 3 = 6 | + 0 | b4 | 6
2 x 6 = 12 | + 0 | b3 | 12
2 x 12 = 24 | + 1 | b2 | 25
2 x 25 = 50 | + 0 | b1 | 50
2 x 50 = 100 | + 1 | b0 | SUM = 101
 |  | Bias + SUM: | 0 + 101 = 101
x

## Slide 19: Two's Complement to Signed Decimal Conversion - Negative
What is 1 1 1 0 0 1 0 1(base 2) in decimal (N)?
Signed Bit Bias | Bit | Bit Position | Bias
-2W-1 = -28-1 = -128 | x 1 | b7 | -128
Product Shift Left | Addend | Bit Position | Product
0 | + 1 | b6 | 1
2 x 1 = 2 | + 1 | b5 | 3
2 x 3 = 6 | + 0 | b4 | 6
2 x 6 = 12 | + 0 | b3 | 12
2 x 12 = 24 | + 1 | b2 | 25
2 x 25 = 50 | + 0 | b1 | 50
2 x 50 = 100 | + 1 | b0 | SUM = 101
 |  | Bias + SUM: | -128 + 101 = -27
x

## Slide 20: Two’s Complement Addition and Subtraction
`
Addition: just add the two number directly
Subtraction: you can convert to addition: difference = minuend + 2’s complement (subtrahend)
x = 0 1 0 1 0 0 1 1
y = 0 0 0 0 1 0 1 1
x + y = 0 1 0 1 1 1 1 0
x-y
x = 0 1 0 1 0 0 1 1
y = 0 0 0 0 1 0 1 1
x = 0 1 0 1 0 0 1 1
x – y = x +(-y) = 0 1 0 0 1 0 0 0
2’s complement first and then add
+ (-y) = 1 1 1 1 0 1 0 1
Cout
0 0 0 0 0 0 1 1
x

## Slide 21: Two’s Complement Positive Overflow
4-bit Two’s complement numbers (positive overflow)
0 1 0 1 5
+ 0 1 1 0 6
1 0 1 1 -5 != 11
Cout
0
0
1
0
SMIN
SMAX
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
0
+ 1
+ 2
+ 3
+ 4
+ 5
+ 6
+ 7
– 8
– 7
– 6
– 5
– 4
– 3
– 2
– 1
Two’s Complement
Overflow: Occurs when an arithmetic result is beyond the min or max limits
x
signed numbers: overflow occurs if
operands have same sign and result’s sign is different

## Slide 22: Two’s Complement Negative Overflow
4-bit Two’s complement numbers (negative overflow)
1 0 0 1 -7
+ 1 0 1 1 -5
0 1 0 0 +4 != -12
Cout
1
1
0
1
signed numbers: overflow occurs if
operands have same sign and result’s sign is different
SMIN
SMAX
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
0
+ 1
+ 2
+ 3
+ 4
+ 5
+ 6
+ 7
– 8
– 7
– 6
– 5
– 4
– 3
– 2
– 1
Two’s Complement
Overflow: Occurs when an arithmetic result is beyond the min or max limits
carry bit is dropped from result
x

## Slide 23: Summary: When Does Overflow Occur
Operand 1
+ Operand 2
Result
Operand 1 Sign | Operand 2 Sign | Is overflow Possible?
+ | + | YES
- | - | YES
+ | - | NO
- | + | NO
x

## Slide 24: Sign Extension in C: Type casts
Convert from smaller to larger integral data types
C and Java automatically performs sign extension
Example (on pi-cluster with 32-bit int and 16-bit short)
x
#include <stdlib.h>
#include <stdio.h>
int main(void)
{
signed char c = -1;
signed int i = c;
unsigned char d = 1;
unsigned int j = d;
printf("c decimal = %hd\n", c);
printf("c = 0x%hhx\n", c);
printf("i decimal = %d\n", i);
printf("i = 0x%x\n", i);
printf("\nd decimal = %hd\n", d);
printf("d = 0x%hhx\n", d);
printf("j decimal = %d\n", j);
printf("j = 0x%x\n", j);
return EXIT_SUCCESS;
}
%./a.out
c decimal = -1
c = 0xff
i decimal = -1
i = 0xffffffff
d decimal = 1
d = 0x1
j decimal = 1
j = 0x1

## Slide 25: Sign Extension (how type promotion works)
Sometimes you need to work with integers encoded with different number of bits
8 bits (char) -> (16 bits) short -> (32 bits) int
Sign extension increases the number of bits: -bit wide signed integer , EXPANDS to a wider n + -bit signed integer where both have the same value
Unsigned
Just add leading zeroes to the left side
Two’s Complement Signed:
If positive, add leading zeroes on the left
  Observe: Positive stay positive
If negative, add leading ones on the left
  Observe: Negative stays negative
• • •
• • •
• • •
• • •
n
original
copies of MSB
x

## Slide 26: Example: Two’s Complement Sign or bit Extension - 1
Adding 0's in front of a positive numbers does not change its value
7 = 0111
extend to
8 bits
00000111
Number is still 7
x
1 = 0001
extend to
8 bits
00000001
Number is still 1

## Slide 27: Example: Two’s Complement Sign or bit Extension -2
Adding 1's if front of a negative number does not change its value
7 = 0111
invert = 1000
add 1 + 1
-7 1001
7 = 00000111
invert = 11111000
add 1 + 1
-7 11111001
-7 = 1001
extend to
8 bits
11111001
x
1001 = -8 + 1 = -7
11111001 =
(-128 + 64 + 32 + 16 + 8) + 1 = -8 + 1 = -7

## Slide 28: Sign Extension Under Different representations
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0
zeroed | original bits
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
s | zeroed | magnitude
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0
sign extension | original bits
1 | 1 | 0 | 1 | 0 | 1 | 1 | 0
How to sign extend this bit pattern?
0xd6
0x00d6
unsigned
0xffd6
two’s
complement
0x8056
signed
magnitude
move the sign bit
(replace original with a 0)
extend the sign bit
x

## Slide 29: Memory Size
Since memory addresses are implemented in hardware using binary
  The Size (number of byte sized cells) of Memory is specified in powers of 2
Memory size/capacity in bytes is specified by the “Number of bits" in an address
  32 bits of address = 232 = 4,294,967,296
  Address Range is 0 to 232 – 1 (unsigned)
Shorthand notation for address size (Memory Capacity)
  KB = 210 (K=1024) kilobyte
  MB = 220 megabyte
  GB = 230 gigabyte
  TB = 240 terabyte
  PB = 250 petabyte
x
Data Bits
Data Bits
Address Bits
Memory dimm

## Slide 30: Different Type of Numbers each have a Fixed # of Bits Spanning one or more contiguous bytes of memory
x
C Data Type | AArch-32 contiguous Bytes
char (arm unsigned) | 1
short int | 2
unsigned short int | 2
int | 4
unsigned int | 4
long int | 4
long long int | 8
float | 4
double | 8
long double | 8
pointer * | 4
0
31
00000000
00000001
00000010
00000011
Word 32-bit integer uses 4 bytes
0
7
15
00000000
000000001
Half Word 16-bit integer uses 2 bytes
0
7
00000000
Byte 8-bit integer uses 1 byte
most significant bit (largest power of 2)
least significant bit (smallest power of 2)
most significant byte
least significant byte

## Slide 31: Byte Ordering of Numbers In Memory: Endianness
Two different ways to place multi-byte integers in a byte addressable memory
Big-endian: Most Significant Byte (“big end”) starts at the lowest (starting) address
Little-endian: Least Significant Byte (“little end”) starts at the lowest (starting) address
Example: 32-bit integer with 4-byte data
a1
b2
c3
d4
0x100
0x101
0x102
0x103
01
23
a1
b2
c3
d4
01
23
d4
c3
b2
a1
Big-Endian
Little-Endian
MSB
Most significant byte
LSB
Least significant byte
x
0x100
0x101
0x102
0x103

## Slide 32: Byte Ordering Example
Decimal: 12345
Binary: 0011 0000 0011 1001
Hex: 3 0 3 9
int x = 12345;
// or x = 0x00003039; // show all 32 bits
39
30
00
00
IA32, ARM32 (little-endian)
30
39
00
00
(big-endian)
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
x

## Slide 33: Byte Addressable Memory Shown as 32-bit words
Observation
32-bit aligned addresses
rightmost 2 bits of the address are always 0
0x12345680
0x12345682
0x12345681
0x12345683
0x00
0x01
0x02
0x03
1 32-bit
(4 byte) word
0x12345684
0x12345686
0x12345687
0x12345685
0x04
0x05
0x06
0x07
1 byte Memory Content
One byte per row
Byte
Memory
Address
1 32-bit
(4 byte) word
Word Aligned address
Word Aligned address
x
0x04
0x05
0x06
0x07
0x00
0x01
0x02
0x03
LSByte
MSByte
0x12345680
0x12345681
0x12345682
0x12345683
Contents of Memory
One 32-bit (4 byte) word per row
0x12345680
0x12345684
Byte address
0x12345688
0x1234568C
0x12345690
0x12345694
Word
Memory
Address

## Slide 34: Do we want to do floating point?

## Slide 35: Scientific Notation Binary
Computer hardware that supports this is called floating point hardware due to the “floating” of the binary point
Declare such variable in C as float (or double)
+1.012 × 2-1
radix (base)
binary point
exponent
mantissa
sign
x

## Slide 36: Floating Point Representation
Analogous to scientific notation
In Decimal:
  Not 12000000, but 1.2 x 107 In C: 1.2e7
  Not 0.0000012, but 1.2 x 10-6 In C: 1.2e-6
In Binary:
  Not 11000.000, but 1.1 x 24
  Not 0.000101, but 1.01 x 2-4
x

## Slide 38: Normalized Scientific Notation
Convert from scientific notation to fixed binary point
Perform the multiplication by shifting the decimal until the exponent disappears
    Example: 1.0112 24 = 101102 = 2210
    Example: 1.0112 2-2 = 0.010112 = 0.3437510
Convert from binary point to normalized scientific notation
  Distribute out exponents until binary point is to the right of a single digit
  Example: 1101.0012 = 1.1010012 x 23
Binary | Decimal
2-1 | 0.5
2-2 | 0.25
2-3 | 0.125
2-4 | 0.0625
x

## Slide 39: Encoding Fractions Observations
In Base 2:
10.1 x 25 = 1.01 x 26
1011.1 x 25 = 1.0111 x 28
0.110 x 25 = 1.10 x 24
Normalizing with base 2 :
adjust so there always a 1 to the left of the decimal point!
this 1 is called the hidden bit as we do not have use a bit to store it since it is there in every normalized mantissa
Adjust x to always be in the format 1.XXXXXXXXX… (fraction is normalized)
Fraction portion ONLY encodes what is to the right of the decimal point
“Hidden bit” allows number to have One additional digit for increased precision
Fraction encoding is 1.[FRACTION BINARY DIGITS]
x

## Slide 40: Floating Point Numbers: Implementation Approach
Supports a wide range of numbers
Flexible “floating” decimal point
Represent scientific notation numbers like 1.202 x
(–1)s M 2E
Sign bit (a single bit): 0 positive, 1 negative
Exponent: encoding of E above (it is NOT E directly represented in binary)
Fraction: encoding of M above (it is NOT M directly represented in binary)
sign bit
exponent
fraction
S
E
M
x

## Slide 41: Excess Bias Encoding (As used in floating point numbers)
Given a number in E bits, to divide the range in about 1/2 the following is used:
excess N bias = (2E-1 – 1) (this is just one of many bias formulas)
With this excess N Bias approach: actual numbers range from most negative to most positive is: -(bias) to bias+1
So, for a number that is limited to 4 bits (0 to 15 unsigned)
  Then excess N bias = 24-1 - 1 = 23 - 1 = a bias of +7
x
actual | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
bias | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7 | +7
bias encoded | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15

## Slide 42: Floating Point Number in a Byte (Not A Real Format)
Mantissa encoding: = 1.[xxxx] encoded as an unsigned value
Exponent encoding: 3 bits encoded as an unsigned value using bias encoding
  Bias encoding = (2E-1 – 1)
  3 bits for the bias we have 23-1 - 1 = 22 - 1 = a bias of 3
  With a Bias of 3: positive and negative numbers range: small to large is: 2-3 to 24
sign bit
exponent
fraction
S = 1 bit
E = 3 bits
M = 4 bits
0
3
4
6
7
1 byte = 8 bits total
Actual | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4
Biased | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Bias | + 3 | + 3 | + 3 | + 3 | + 3 | + 3 | + 3 | +3
x

## Slide 43: Scientific Notation Decimal
Scientific Normalized form:
exactly one digit (non-zero) to left of decimal point
Alternatives to representing 1/1,000,000,000
  Normalized: 1.0×10-9
  Not normalized: 0.1×10-8, 10.0×10-10
+6.0210 × 1023
radix (base)
decimal point
exponent
mantissa
sign
x

## Slide 44: Floating Point Number in a Byte (Not A Real Format)
Mantissa encoding: = 1.[xxxx] encoded as an unsigned value
Exponent encoding: 3 bits encoded as an unsigned value using bias encoding
  Bias encoding = (2E-1 – 1)
  3 bits for the bias we have 23-1 - 1 = 22 - 1 = a bias of 3
  With a Bias of 3: positive and negative numbers range: small to large is: 2-3 to 24
sign bit
exponent
fraction
S = 1 bit
E = 3 bits
M = 4 bits
0
3
4
6
7
1 byte = 8 bits total
Actual | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4
Biased | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Bias | + 3 | + 3 | + 3 | + 3 | + 3 | + 3 | + 3 | +3
x

## Slide 45: Floating Point Number (8-bits) Number Range: 2-3 to 24
sign bit
exponent
fraction
S = 1 bit
E = 3 bits
M = 4 bits
0
000
0000
S = 1 bit
E = 3 bits
M = 4 bits
0.0 Special case in this simple model
we do not put back the “hidden bit”
0
000
0001
S = 1 bit
E = 3 bits
M = 4 bits
Smallest Non-zero Positive
0.0010001 = 1/8 + 1/128 = 0.1328125 base 10
0/1
111
1111
S = 1 bit
E = 3 bits
M = 4 bits
Largest Positive/Negative
1.1111 x 24 = 11111 = 31 base 10
1
000
0000
S = 1 bit
E = 3 bits
M = 4 bits
Smallest (closest to zero) Number
1.0000 x 2-3 = 0.001000 = 1/8 = -0.125 base 10
Note: Orange is hidden bit added back
x

## Slide 46: Decimal to Float
Step 1: convert from base 10 to binary (absolute value)
-0.375(decimal) = 0000.01102
Step 2: Find out how many places to shift to get the number into the normalized 1.xxxx mantissa format
0000.01102 = 1.1000 x (2-2)base 10
exponent: -210 + bias of 310 = 110 = 0b001 for the exponent (after adding the bias)
Step 3: Use as many digits that fit to the right of the decimal point in the fractional .xxxx part 1.1000
Step 4: Sign bit
positive sign bit is 0
negative sign bit is 1
7 | 6 |  |  |  | 4 | 3 |  |  |  |  | 0
s | exponent (3 bits) |  |  |  |  | fraction (4 bits) |  |  |  |  | 
Bias of 3
s | exponent | fraction
1 | 0b001 | 0b1000
0x9 |  | 0x8
= 0x98
x

## Slide 47: Float to Decimal
Step 1: Break into binary fields
0x45 =
Step 2: Extract the unbiased exponent
0b100 = 4base 10 - bias of 310 = 110 for the exponent (bias removed)
Step 3: Express the mantissa (restore the hidden bit)
1.0101
Step 4: Apply the unbiased exponent
1.0101base 2 x (21)base 10 = 10.101
Step 5: Convert to decimal
10.101 = 2.625base 10
Step 6: Apply the Sign
+ 2.625base 10
7 | 6 |  |  |  | 4 | 3 |  |  |  |  | 0
s | exponent (3 bits) |  |  |  |  | fraction (4 bits) |  |  |  |  | 
Bias of 3
0x4 |  | 0x5
s | exponent | fraction
0 | 0b100 | 0b0101
x

## Slide 48: IEEE “754” Floating Point Double and Single Precision
31 | 30 |  | 23 | 22 |  |  |  |  | 0
sign | Exponent (8 bits) Uses a Bias of 127 |  |  | fraction (23 bits) |  |  |  |  | 
63 | 62 |  | 52 | 51 |  |  |  |  | 0
sign | Exponent (11 bits) Uses a Bias of 1023 |  |  | fraction (52 bits) |  |  |  |  | 
Single Precision (C float)
x 1.fraction
Double Precision (C Double)
x 1.fraction
x

## Slide 49: Convert 2.5 to IEEE754 format
31 | 30 |  | 23 | 22 |  |  |  |  | 0
sign | Exponent (8 bits) Uses a Bias of 127 |  |  | fraction (23 bits) |  |  |  |  | 
Single Precision (C float)
x 1.fraction
x

## Slide 50: What is the equivalent of 0xC1590000
31 | 30 |  | 23 | 22 |  |  |  |  | 0
sign | Exponent (8 bits) Uses a Bias of 127 |  |  | fraction (23 bits) |  |  |  |  | 
Single Precision (C float)
x 1.fraction
x

## Slide 51: Extra slides

## Slide 52: Another Way to Look at 2's Complement Encoding
A 2's compliment value can be thought of as using a slightly different bias encoding for negative numbers only (more negative values): -2W-1
The leftmost bit is then interpreted as a decision to apply the bias (if 1) or not (if 0)
  1 apply the bias
  0 do not apply the bias
For example, for a 4-bit number (w = 4) , the negative number bias weight would be = = -23 = -8
Observe: adding +1 makes the number more positive for both negative and positive numbers
3 bit | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111 | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
Actual | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
+Bias | -8 | -8 | -8 | -8 | -8 | -8 | -8 | -8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
decimal | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
2's | 1000 | 1001 | 1010 | 1011 | 1100 | 1101 | 1110 | 1111 | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111
x

## Slide 53: Decimal to IEEE Single Precision Float
Step 1: convert from base 10 to binary (absolute value)
-13.375(decimal) = 1101.0110
Step 2: Find out how many places to shift to get the number into the normalized 1.xxxx mantissa format
1101.0110 = 1.1010110 x (23)base 10
3 + bias of 127 = 130 for the exponent = 0b1000 0010
Step 3: Use as many digits that fit to the right of the decimal point in the fractional .xxxx part (0 pad )
1.1010110 0000 0000 0000 0000
Step 4: If the sign is positive sign bit is 0, otherwise it is 1
s | exponent | fraction
1 | 100 0001 0 | 101 0110 0000 0000 0000 0000
31 | 30 |  | 23 | 22 |  |  |  |  | 0
sign | Exponent (8 bits) Bias is 127 |  |  | fraction (23 bits) |  |  |  |  | 
= 0xc1560000
0xc
0x1
0x5
0x6
0x0
0x0
0x0
0x0
x

## Slide 54: IEEE Single Precision Float to Decimal
Step 1: Break into binary fields and expand as needed
0xc0b00000 =
Step 2: Find the exponent
0b10000001 = 129base 10 - bias of 12710 = 210 exponent with bias added
Step 3: Express the mantissa (restore the hidden bit)
1.0110
Step 4: Apply the exponent
1.0110 x (22)base 10 = 101.10
Step 5: Convert to decimal
101.10 = 5.5
Step 6: Apply the Sign
-5.5
1 | 100 0000 1 | 011 0000 0000 0000 0000 0000
31 | 30 |  | 23 | 22 |  |  |  |  | 0
sign | Exponent (8 bits) Bias is 12710 |  |  | fraction (23 bits) |  |  |  |  | 
0xc
0x0
0xb
0x0
0x0
0x0
0x0
0x0
x